## Slide 1: Cube stacking assistant
System architecture: motion-gated YOLO + geometric reasoning, a goal set from an image, and a VLM (Qwen3-VL via Ollama) called only on anomalies
goal, bottom to top
Notes: Title slide. The cube stack on the right is the motif used through the deck: red, green, black, white, bottom to top.

## Slide 2: End-to-end architecture
OAK-D Pro camera
RGB 1280×720 @ 30 fps
white balance locked
Motion gate
IDLE · MOVING · SETTLING · CONFIRMING
YOLO only after the scene settles
YOLO detector
cube colour class + box
best.pt, conf ≥ 0.25
Geometric reasoning
colour check · side-face merge
stack grouping · hidden-cube probe
reading: stacks bottom → top + table cubes
Goal setup
live capture · --goal-image
--goal r,g,b,w
Order check vs goal
complete · in progress · wrong
+ exact anomaly
Anomaly?
Code planner
instant step-by-step moves
no VLM call
no
yes
VLM check: Qwen3-VL via Ollama (background thread)
LOOK
raw image →
stacks bottom→top
GROUND
boxes for cubes
YOLO missed
PLAN + verify
moves replayed in
code; code fallback
Outputs
GUI panel: verdict + steps
per settle: 4 images + result.json
session log
Colour key
Input + gating
Perception
Goal + decision
Code planner
VLM
Outputs
Every settle is saved (images + JSON) whether or not the VLM is called. The camera loop never waits for the VLM.
Notes: Main flow: frames are gated by motion; once the scene settles YOLO and the geometric reasoning produce a reading bottom to top. It is compared with the goal. No anomaly: the code planner answers instantly. Anomaly: the VLM reads the raw image, places the cubes YOLO missed, and plans the moves, which code verifies.

## Slide 3: Start-up and goal setup
Start script
parse arguments
Check Ollama
model tag matched
ignoring case
Load YOLO
class names →
known colours
Set the goal
one of 3 sources
(below)
Live monitoring
motion-gated loop
1
Default: live capture
Window shows "SET THE GOAL"
Build the target stack, press SPACE
Reading shown with boxes: ENTER accepts, SPACE captures again
2
--goal-image FILE
Photo of the target stack
Read once at start, no confirmation
Needed with --image (single-image mode)
3
--goal red,green,black,white
Order given directly, bottom → top
Colours checked against the YOLO classes
No photo needed
How a goal photo is read: YOLO + geometric reasoning, then the VLM LOOK on the raw image; the tallest stack is the goal. Saved in result/goal/goal_<time>/ (photo, annotated photo, goal.json).
Notes: The goal is no longer hard-coded. Every settle JSON records the goal and its source.

## Slide 4: Motion gate: run YOLO only when the scene settles
IDLE
last result shown
MOVING
boxes hidden
SETTLING
motion → restart clock
CONFIRMING
YOLO on every frame
motion in work area
(2 frames > 1 % changed)
frame looks still
still for 0.7 s
3 matching YOLO results
→ NEW SETTLE
hand returns
heartbeat 5 s
How it works
Motion = colour change against an anchor frame, in the work area set with the a key
Comparing with an anchor, not the last frame, catches a slow hand
CONFIRMING ends when 3 YOLO readings agree (or the majority after 15)
Every settle after real motion is saved, even if the reading did not change
A heartbeat counts only if the reading changed
Notes: Parameters: SETTLE_SECONDS 0.7, CONFIRM_FRAMES 3, CONFIRM_MAX_FRAMES 15, HEARTBEAT_SECONDS 5, MOTION_AREA_FRAC 1 %.

## Slide 5: Perception: YOLO + geometric reasoning
1
YOLO detector
Class (red / green / black / white) and box for each visible cube. Often misses: the bottom cube of a stack, cubes in shadow, white against a white wall.
2
Colour check
HSV of the box centre. An unsaturated "red" or "green" is relabelled white or black; a bright "black" box is rejected.
3
Duplicate + side-face merge
Same-colour boxes side by side are one turned cube: the most confident box is kept. Boxes with width / height < 0.6 are side faces.
4
Stack grouping
Boxes in one column with similar width form a stack, sorted bottom → top by height in the image. Side faces join the column they touch.
5
Hidden-cube probe
One cube-step below each stack: if every cell of a 3×3 grid matches one cube colour, a cube is inferred: dashed box, "(geometric reasoning)".
6
Reading
Stacks bottom → top plus single table cubes, e.g. red>green>black | white. Passed to the order check against the goal.
Notes: Steps 2-5 are the geometric reasoning. Image 2 of each settle shows step 1 only, image 3 shows the result of step 6.

## Slide 6: When is the VLM called? Only on an anomaly
Trigger | Meaning | Example (goal r>g>b>w)
Wrong order | A stacked cube is not the goal cube for its position | stack r > g > w
Cube not seen | A goal cube is detected nowhere: YOLO probably missed it | white not found
Gap in a stack | Spacing in a stack far larger than usual: a cube may be hidden | r > [gap] > b
v key | Manual check by the worker | any scene
Not an anomaly: a complete stack, or a stack that is correct so far with the remaining cubes on the table. The code planner answers at once and the panel says "VLM not called: no anomaly against the goal".
No anomaly
in progress → code planner:
1. Put WHITE on BLACK
Anomaly
wrong order → VLM checks:
1. WHITE to the table
2. BLACK on GREEN
3. WHITE on BLACK
Notes: Trade-off: if YOLO misses the top cube of a stack that is otherwise correct, it looks like normal progress and the VLM is not called; press v.

## Slide 7: VLM check: LOOK → GROUND → PLAN
1
LOOK
Read the scene
Input: raw settled frame, no boxes or YOLO hints (768 px)
Output (JSON schema): stacks [[bottom … top]], table [ … ]
Rejected if a colour is listed twice or a confident YOLO cube (≥ 0.6) is missing
Re-asked once with the reason, else the YOLO reading is used
2
GROUND
Locate missed cubes
Only for cubes the VLM found but YOLO did not
Image padded to a 1000×1000 square, so pixel and 0–1000 coordinates agree
Output: boxes [{colour, box}]
Box used only if its size, place and colour fit
3
PLAN + verify
Fix the stack
Text only: accepted reading + goal + worked example
Output: status, problem, moves [{cube, to}]
Code replays every move: legal? goal reached? status matches the order check?
Re-asked up to 2× with the reason, else the code planner
Making a small local VLM reliable
Ollama REST on localhost:11434, think = false
Answers forced into a JSON schema; JSON recovered from "thinking" if needed
Runs in the VLMWorker thread; every settle is queued in order
A bad answer never blocks: code fallbacks always give steps
Notes: Default model qwen3-vl:8b (also tested gemma4:31b as an option). Code always has the last word on the order check.

## Slide 8: Final annotation: where each box comes from
1
YOLO box
Detected box of that colour that fits the stack column best
2
VLM box
GROUND box, if its size, position and colour check out (white: size + position only)
3
Colour fit
Cube-sized blob of that colour where the cube must be
4
Estimate
One cube-step above / below the neighbour, step measured from the stack
Used in order: the first that works wins.
How boxes are drawn
S1-2 green
YOLO detection
S1-1 red (geometric reasoning)
hidden-cube probe
S1-4 white (VLM)
found only by the VLM
YOLO boxes the VLM rejected (e.g. a laptop corner) are not drawn; they are listed in result.json as ignored_detections.
Notes: Tag S1-2 = stack 1 (numbered left to right), 2nd cube from the bottom.

## Slide 9: Outputs for every settle
result/
goal/goal_<time>/
goal_raw.jpg, goal_annotated.jpg, goal.json
settles/settle_<time>/
1_raw.jpg clean frame
2_yolo_only.jpg plain YOLO boxes
3_yolo_geometric.jpg + geometric reasoning
4_final_vlm.jpg final reading + panel
result.json
stack_log_vlm_<session>.txt
snapshot_<time>.jpg / _stack.txt (s key)
goal
order bottom → top + source
yolo_only
raw YOLO boxes, bottom → top
detector
YOLO + geometry: stacks, verdict, per-cube source
vlm
called? trigger, reading, raw replies, boxes
comparison
missed by YOLO / by VLM, placed differently
final
reading, status, instructions, moves, boxes
Notes: result.json sections. All stacks are listed bottom to top so they can be compared directly with the goal.

## Slide 10: Runtime: two threads, nothing blocks the camera
Main thread
(camera loop)
VLM worker
thread
Read frame
OAK-D, newest only
Motion gate
state machine
YOLO + geometry
on settle
Save images 1-3
settle folder
Anomaly?
vs goal
Code result
image 4 + JSON
no
yes: job queued (every settle, in order)
Take next job
queue
LOOK
raw image
GROUND
missed cubes
PLAN + verify
code fallback
Image 4 + JSON
GUI updated
Keys
q
quit (pending checks finish first)
s
snapshot
p
pause
i
info line
d
debug detections
a
work area
r
re-check
v
force VLM
Notes: If the VLM thread hits an error on one settle, that settle still gets image 4 and JSON with a note; the thread carries on.

## Slide 11: Key configuration parameters
Parameter | Default | Effect
VLM_MODEL | qwen3-vl:8b | Vision model in Ollama (tag case ignored)
VLM_ON_ANOMALY_ONLY | True | False = call the VLM on every settle
VLM_ANNOTATE | False | VLM sees the raw image (True: YOLO boxes drawn)
VLM_GROUND / NO_COLOUR_CHECK | True / ('white',) | Ask for missed-cube boxes; colours not checked by pixels
VLM_LOOK_RETRIES / VLM_PLAN_RETRIES | 1 / 2 | Re-asks with the reason before falling back
VLM_TRUST_CONF | 0.6 | YOLO cubes the VLM must not drop
CONF | 0.25 | YOLO confidence threshold
SETTLE_SECONDS / CONFIRM_FRAMES | 0.7 / 3 | Stillness before YOLO; readings that must agree
MOTION_AREA_FRAC | 0.01 | Changed share of the work area that counts as motion
SIDE_FACE_ASPECT / MERGE_X_GAP | 0.6 / 0.2 | Side-face width ratio; gap for same-cube merge
PROBE_CELL_MIN_FRAC | 0.5 | Hidden-cube probe: colour share per grid cell
MANUAL_WB_K | 4000 | OAK white balance lock (K)
Notes: All parameters live at the top of detect_stack_live_vlm.py.